## Slide 1: Extending the Reach of GPS-assisted Femtocell Synchronization and Localization through Tightly-Coupled Opportunistic Navigation
Ken Pesyna, Kyle Wesson, Robert Heath Jr., Todd Humphreys
Presentation at Globecom 2011 | December 5, 2011

## Slide 2: Why Synchronization & Localization?
Ensure reliable handover
Reduce interference
Operate within licensed spectrum
Locate emergency calls
Synchronization and Localization are key requirements for femtocells

## Slide 3: Challenges of Satellite-based Synchronization
Femtocells placed indoors
GPS signals weak: -155 dBW
Up to 45 dB penetration loss

## Slide 4: Time and Frequency Requirements
Minimum synchronization requirements [Rakon]:
Chart: Requirements by Cellular Standard
| 10
CDMA2000 | 100
GSM | 100
WiMAX | 500
LTE | 250
WCDMA | 250
TD-SCDMA | 100
These are very stringent requirements!

## Slide 5: Location Requirements
Spectrum licensing & operator control
Emergency caller location identification (E911)
10m
20km
E911
Spectrum Licensing
Challenging!
Big Issue: E911

## Slide 6: Prior Work
Chart: Time Requirement (us)
| 10
CDMA2000 | 100
GSM | 100
WiMAX | 500
LTE | 250
WCDMA | 250
TD-SCDMA | 100
Precision time protocol (PTP) [Eidson02]
Cellular network listen [Edwards08]
GPS-based solutions [Lewandowski99, Smith09]
20km
50 - 300m
5m
1-20 km
10m

## Slide 7: Challenges of GPS
High signal sensitivity is required to acquire GPS signals indoors
  5 dB-Hz to cover 90% of residences
Sensitivity attainable today:
  State-of-the art via EGPS/AGPS is 14 dB-Hz [RoDuJaGra08]
Goal: Close this 9 dB gap

## Slide 8: Closing the 9 dB gap: Requirements
Coherently integrate GPS signal over extended interval
  Local oscillator drifts
     This requires a more stable oscillator
  # of time-frequency search cells explodes
    Increases probability of false alarm
     The search space must be reduced

## Slide 9: Proposed Solution: Tightly-Coupled Opportunistic Navigation
Use ambient radio “signals of opportunity”:
  Stabilize femtocell’s local oscillator
  Narrow the GPS search space
Cellular
HDTV

## Slide 10: Tightly-Coupled Opportunistic Navigation
Final
Accumulation
Estimator

## Slide 11: Benefits of Proposed TCON
  Frequency stability transfer
    Correct its local clock variations to allow extended integration
  Search space contraint
    Aiding of precise time and frequency information
    Decreases time & frequency uncertainty

## Slide 12: Ambient Signal Analysis
Analyzed ambient CDMA signals
Extremely stable and synchronous
  Signals remain stable beyond 9 seconds
  Time synchronized to 4 µs (2 of 3)
  Frequency accurate to 0.3 Hz
Mean-squared Coherence vs Time
9.5 s
20 s
100+ s

## Slide 13: Field Demonstration
Cellular CDMA signals recorded in Austin, TX
TCON used to estimate the local clock variations using only CDMA signals

## Slide 14: Conclusions
Synchronization is required for femtocell operation
Location is required to meet FCC regulations
Existing approaches may not meet requirements
Propose TCON to exploit other available signals
Increases the GPS-sensitivity of the femtocell
  GPS meets the syncrhonization requirements
  Allows femtocells to be located further indoors

## Slide 15: Conclusions
Requirements to acquire a 5 dB-Hz GPS signal:
  Coherent integration time of 7 seconds
  Time certainty to within 6 µs of GPS time
  Frequency certainty to within 0.5 Hz
TCON achieves the needed gain in sensitivity
Femtocells synchronized indoors using GPS

## Slide 16
Questions?