## Slide 1
GPS Spoofing & Implications for Telecom
Kyle Wesson
The University of Texas at Austin
Sprint Synchronization Conference | September 18, 2013

## Slide 2: Talk Overview
Civil GPS Spoofing Vulnerability
Anti-Spoofing Techniques
  Cryptographic: Navigation Message Authentication
  Non-Cryptographic: “Sandwich” Defense
Securing and Testing

## Slide 3: Civil GPS is Vulnerable to Spoofing
An open GPS standard makes GPS popular but also vulnerable to spoofing
[HumLed&08]

## Slide 4
University of Texas Spoofing Testbed

## Slide 5: Inside a Spoofing Attack

## Slide 6: Civil GPS Spoofing
A discrete spoofing attack typically involves four phases:
  Alignment of the authentic and spoofed GPS signals at the target receiver
  Increase the power of the spoofed signals above the authentic
  Move the spoofed signals slowly away from the authentic signals
  Once the spoofed and authentic signals no longer interfere, the spoofer has complete control of the target receiver’s PVT solution
Spoofer-imposed dynamics are limited only by the bandwidth of the target receiver’s tracking loops and it’s quality indicators
No receiver we’ve tested has ever successfully defended against this type of attack
D.P. Shepard and T.E. Humphreys, “Characterization of Receiver Response to Spoofing Attacks,” Proceedings of ION GNSS, Portland, Oregon, 2011.

## Slide 7: Spoofing a UAV (2012)
Internet or LAN
Receive Antenna
External Reference Clock
Control Computer
GPS Spoofer
UAV coordinates from tracking system
Transmit Antenna
Spoofed Signals as a
“Virtual Tractor Beam”
Target UAV

## Slide 8: Surprises (1/2)
Receiver Autonomous Integrity Monitoring (RAIM) was helpful for spoofing: we couldn’t spoof all signals seen by unmanned aerial vehicle (UAV) due to our reference antenna placement, but the Hornet Mini’s uBlox receiver rejected observables from authentic signals, presumably via RAIM
Overwhelming power is required for clean capture: A gradual takeover leads to large (50-100 m) multipath-type errors as the authentic and counterfeit signals interact
The UAV’s heavy reliance on altimeter for vertical position was easily overcome by a large vertical GPS velocity

## Slide 9: Surprises (2/2)
Not possible even to station keep with a captured UAV based on visual position estimates: GPS capture breaks flight controller’s feedback loop; now spoofer must play the role formerly assumed by GPS. Implication: An accurate radar or LIDAR system would be required for fine “control” of UAV via spoofing
Compensating for all system and geometric delays to achieve meter-level alignment is challenging but quite possible

## Slide 10: Spoofing a Super Yacht (2013)

## Slide 11: Telecom Network Vulnerabilities
In 35 minutes, spoofer can shift time 10 μs, which would disrupt CDMA2000 call hand-off
Standard | Timing (Air) | Frequency (Transport / Air)
CDMA2000 | ± 3 – 10 µs | ± 16 ppb / ± 50 ppb
GSM | – | ± 16 ppb / ± 50 ppb
LTE (FDD) | – | ± 16 ppb / ± 50 ppb
LTE (TDD) | ± 1.5 µs | ± 16 ppb / ± 50 ppb
TD-SCDMA | ± 1.5 µs | ± 16 ppb / ± 50 ppb

## Slide 12: Misconceptions about Timing Security (1/2)
“Holdover” capability of GPS-disciplined oscillator (GPSDO) protects against spoofing
  Holdover will not be triggered by a sophisticated spoofing attack
The reference oscillator’s drift rate is the upper limit of speed at which a GPSDO can be spoofed (e.g., 1 us per day)
  Drift rate only matters if GPSDO is configured to alarm on a mismatch between GPS rate and internal clock rate
  Even then, spoofer can push GPS timing at about 5x the calibrated clock drift rate because of need to keep false alarm rate low

## Slide 13: Misconceptions about Timing Security (2/2)
Timing errors only become a problem at the level of seconds, or maybe milliseconds.
  Microseconds matter in comm, finance, and energy sectors
Cross-checking against an atomic clock affords foolproof timing security
  Rubidium clock with stability of 10-12 can be pushed off by about 100 ns per day
PTP/NTP are a potential solution to GPS spoofing problem
  These are getting better, but, due to network asymmetry, they still not accurate enough for most demanding applications non-dedicated networks

## Slide 14: Recommendations
Require navigation systems for UAVs above 18 lbs to be certified “spoof-resistant”
Require navigation and timing systems in critical infrastructure to be certified “spoof-resistant”
“Spoof resistant” defined by ability to withstand or detect civil GPS spoofing in a battery of tests performed in a spoofing testbed (e.g., Texas Spoofing Battery)
Humphreys’ testimony to House Committee on Homeland Security, July 19, 2012

## Slide 15: Anti-Spoofing

## Slide 16
Spoofing Defenses
Cryptographic
Non-Cryptographic
Stand-Alone
Networked
J/N Sensing
(Ward, Scott, Calgary)
SSSC or NMA on WAAS
(Scott, UT)
Single-Antenna Spatial Correlation
(Cornell, Calgary)
SSSC on L1C
(Scott)
Correlation Anomaly Defense
(TENCAP, Ledvina, Torino, UT)
Sensor Diversity Defense
(DARPA, BAE, UT)
NMA on L2C, L5, or L1C
(MITRE, Scott, UT)
P(Y) Cross-Correlation
(Stanford, Cornell)
Multi-Element Antenna Defense
(Keys, Montgomery, DLR, Stanford)

## Slide 17: Cryptographic Anti-Spoofing
Anti-Spoofing

## Slide 18: Security-Enhanced GPS Signal Model
Security code :
  Generalization of binary modulating sequence
  Either fully encrypted or contains periodic authentication codes
  Unpredictable prior to broadcast

## Slide 19: Attacking Security-Enhanced GPS Signals
Record and Playback (Meaconing): record and re-broadcast RF spectrum
Security Code Estimation and Replay (SCER) Attack: estimate security code on-the-fly without additional noise
re-broadcast with delay and amplitude
security code estimate

## Slide 20: How to authenticate a GPS signal?
[WesRot&12]
Code Origin Authentication
Code Timing Authentication
Metrics
Standard Receiver

## Slide 21: Declaring a Signal Authentic
  From time of verifiable non-spoofing event:
  Logical remained low
  Logical remained low
  remains above acceptable threshold

## Slide 22: Embedding the Signature
Civil Navigation (CNAV) Message
  Flexible & extensible
Packet-like structure:
  300 bits in 12 sec
  Message Type ID field can identify up to 64 messages of which only 15 are defined

## Slide 23: Non-Cryptographic Anti-Spoofing
Anti-Spoofing

## Slide 24: Spoofing Requirement and Difficulty
Q: What is a requirement of a successful spoofing attack?
A: Spoofed signal power greater than authentic signal power
Q: What is a difficulty of a successful spoofing attack?
A: Suppressing authentic signals while remaining below J/N sensor detector

## Slide 25: “Sandwich” Defense
Constrain spoofer between
  total in-band received power detector &
  cross-correlation function distortion monitor
Features
  Use multiple correlator taps (RAKE-like)
  Check multipath signatures across channels
  Real-time, software defense

## Slide 26: Spoofed Signal Distortions

## Slide 27: Clean vs. Spoofed Scenarios
Nominal Power and Minimal Distortions
Additional Power and Large Distortions

## Slide 28: Securing and testing
So what is there to do?

## Slide 29: Options for Secure ns-Accurate Timing (1/2)
Obtain required permissions to purchase SAASM-equipped GPSDO
  Lots of paperwork, special handling
  Expensive
  Fairly secure against spoofing
  Not secure against replay attack
Wait for GPS Directorate to insert digital signatures into modernized GPS signals
  They’re making progress! (The University of Texas is helping.)
  Not so strong as SAASM for timing security, but quite effective
  Eventually inexpensive, but will require new GPSRO

## Slide 30: Options for Secure ns-Accurate Timing (2/2)
Cross-check GPS timing against redundant high-quality (e.g., atomic) clocks
  Self-contained
  Expensive
  Absolutely secure to within about 5x the drift rate of ensemble
“All Signals” Approach: Develop a GPSDO that pulls in signals from GPS + Glonass + Galileo and rigorously cross-checks these
  None on market yet (so far as I’m aware)
  Potentially inexpensive: uBlox LEA-7 runs ~$50
  Spoofer’s job gets much harder with each new signal
PTP/NTP over a dedicated network

## Slide 31
The Texas Spoofing Test Battery (TEXBAT)
6 high-fidelity recordings of live spoofing attacks
  20-MHz bandwidth
  16-bit quantization
  Each recording ~7 min. long; ~40 GB
Can be replayed into any GNSS receiver

## Slide 32
The University of Texas Radionavigation Lab
and
National Instruments
jointly offer the Texas Spoofing Test Battery
Request: todd.humphreys@mail.utexas.edu
The Dynamic Matched-Power Position Push
The Dynamic Overpowered Time Push
The Static Matched-Power Position Push
The Static Matched-Power Time Push
The Static Overpowered Time Push
The Static Switch
FREE

## Slide 33: Observations on Defenses
Crypto defenses not a panacea: Ineffective against near-zero-delay meaconing (entire band record and playback) attacks.
Non-crypto defenses not so elegant mathematically, but can be quite effective.
Best shield: a coupled crypto-non-crypto defense.
When implemented properly, navigation message authentication (NMA) authenticates not only the data message but also the underlying signal. It is surprisingly effective.

## Slide 34: Thank you
email: kyle.wesson@utexas.edu
web: http://radionavlab.ae.utexas.edu

## Slide 35: Radionavigation
GPS
GNSS
Radionavigation
Systems
GPS
GNSS
Radionavigation
Systems
Notes: The scope of our research in the UT Radionavigation Laboratory covers GPS, GNSS, and other radionavigation systems -- or systems that can be repurposed as radionavigation systems -- such as the Iridium low-earth-orbiting communications constellation, HDTV, cellular telephony systems, and the NIST timing dissemination system. We’re also looking to create our own local navigation systems: ad-hoc collaborative radionavigation networks in which each node benefits from assistance data and ranging signals transmitted by the other nodes. Hence, GPS is at the core of our work, but our scope extends well beyond it.

## Slide 36: GPS Errors & Accuracy
Ephemeris errors in r i: 2 m
Transmitter clock errors: 2 m
Residual Ionospheric delay: 4 m*
Tropospheric delay: 0.5 m
Multipath (reflected signals): 1 m#
Receiver noise: 0.5 m
Multiplicative effect of geometry (GDOP)
Typical accuracy: 10 m/axis, 30 nsec in time, 0.01 m/sec velocity
  * for single-frequency receiver w/model corrections, error > 15 m possible in unusual ionospheric conditions, low elevation
  # error > 15 m possible in strong multipath environments
Notes: Be sure mention GDOP as a multiplicative factor and the final accuracies.

## Slide 38: Smart Grid Vulnerabilities
Operational system in Mexico on the Chicoasen-Angostura transmission line
  Automated PMU-based control
  Connects large hydroelectric generators to large loads
  Two 400-kV lines and a 115-kV line
Large phase angle offsets (>10○) induced in minutes
  Protects against generator instability during double fault by shutting down generators
Spoofing attack can cause PMUs to violate IEEE C37.118 Standard
[SheHum&12]

## Slide 39
Navigation signal authentication is hard. Nothing is foolproof. There are no guarantees. But simple measures can vastly decrease the probability of a successful attack. Probability is the language of anti-spoofing.
Symmetric-key systems (e.g., SAASM) offer short time to authenticate but require key management and tamper-proof hardware: more costly, less convenient. SAASM and M-code will never be a solution for a wide swath of applications (e.g., civil aviation, low-cost location and time authentication).
Observations on Defenses (1/3)

## Slide 40
Asymmetric-key (public-private key) systems have an unavoidable delay (e.g., 40 seconds between authentication of any signal) but delay can be accepted in many applications; also, for non-complicit spoofing there is no need to tamper-proof the receiver: cheaper, more convenient.
Proof of location (proving to you where I am) is emerging as a vital security feature. It’s not easy: non-crypto approaches require elaborate tamper proofing; crypto approaches require high-rate security code. Beware black-market vendors with high-gain antennas who will sell an authenticated location.
Observations on Defenses (2/3)

## Slide 41
Crypto defenses not a panacea: Ineffective against near-zero-delay meaconing (entire band record and playback) attacks.
Non-crypto defenses not so elegant mathematically, but can be quite effective.
Best shield: a coupled crypto-non-crypto defense.
When implemented properly, navigation message authentication (NMA) authenticates not only the data message but also the underlying signal. It is surprisingly effective.
Observations on Defenses (3/3)

## Slide 42
TEXBAT Recording Setup

## Slide 43
Scenario 2: Static Overpowered Time Push

## Slide 44: GNSS Signal Processing Basics

## Slide 45: GNSS Signal Processing Basics

## Slide 46: GNSS Receiver Block Diagram
Notes: Correlation: correlate with code to produce prompt, early, late complex accumulation phasors
Coherent summations: For weak signals (C/N0 < 45dB) M of them
Code Tracking: Phase Detector & Code Loop Filter
Carrier Tracking: Carrier Phase Detector & Carrier Phase Loop Filter
Code Generator: Generate delayed code (like a long measuring tape of consecutive codes)
NCO: Integrator
Why Carrier-Aided Code Tracking instead of Code-Only Tracking?
Code @ 1.023 MHz & Carrier @ 1575.42 MHz -> Code wavelength @ 300 m & Carrier wavelength @ 19 cm
To get same precision in code as in carrier we need a filter with a time constant 1,000 times as high as carrier. But for typical Noise scenarios and fD dynamics (Bwcode ~ 0.2 Hz and Bwcarrier ~ 20 Hz) stable code-loop only filter are impossible to realize.